## Slide 1: Balances
Mosab Nouraldein Mohammed
Musab.noor13@gmail.com

## Slide 2: I BASIC PRINCIPLES
Weight is the force of gravity on an object.
Balances measure this force.

## Slide 3: WEIGHT versus MASS
Mass: amount of matter in an object; units are kilograms.
Mass doesn’t change when object is moved to new location.
  Astronaut is “weightless” in space but mass is the same.
In the lab, we weigh objects.

## Slide 4: WEIGHING AN OBJECT
We compare pull of gravity on sample with pull of gravity on standard(s) of established mass.

## Slide 5: BASIC BALANCE
When the beam is exactly balanced, gravity is pulling equally on sample and standard they are the same weight.
Hence named “balances”.

## Slide 6: OLDEST SCIENTIFIC INSTRUMENTS
Mechanical balances have one or more beams; objects are placed on a pan attached to a beam.
Have been used for hundreds of years.

## Slide 7: MECHANICAL BALANCES
Still used for some purposes – balancing centrifuge tubes.

## Slide 8: ELECTRONIC BALANCES
Still measure pull of gravity on objects but do not have beams.
Use an electromagnetic force rather than weights to counterbalance the sample.

## Slide 9: ELECTRONIC BALANCES
Produce an electrical signal when a sample is placed on the weighing pan, the magnitude of which is related to the sample’s weight.
To convert electrical signal to a weight value, balance compares the electrical signal from the sample to the signal from a standard(s) of known weight.

## Slide 10: ELECTRONIC BALANCES
Electronic balances make the comparison between sample and standard sequentially:
  Calibrate with a standard at one time
  Later the sample is weighed

## Slide 11: II CHARACTERISTICS AND TYPES OF BALANCES
Range is the span from the lightest to the heaviest weight the balance can measure.
Capacity is the heaviest sample balance can weigh.

## Slide 12: SENSITIVITY AND READABILITY
Sensitivity: smallest weight that will cause a change in the response of the balance.
    Sensitivity determines the number of places to the right of the decimal point that the balance can read accurately and reproducibly.

## Slide 13
    Extremely sensitive balances weigh accurately to the nearest 0.1 microgram (or 0.0000001 g).
    Less sensitive balance might read to the nearest 0.1 gram. Manufacturers express the sensitivity of their balances by their readability.

## Slide 14
Readability: The smallest fraction of the scale division that can be read. The validity of this reading depends on the precision of the instrument.
Precision: The degree of agreement between repeated weighting's of the same mass.

## Slide 15
Accuracy: The agreement between the result of measurement and the true value of the quantity measured . Balance: An instrument for the comparison of weight.

## Slide 16: ANALYTICAL BALANCES
Analytical balances optimize sensitivity and can weigh samples to at least the nearest tenth of a milligram (0.0001 g).
Are both mechanical and electronic balances of all types.

## Slide 17: RANGE, CAPACITY, SENSITIVITY
Range, capacity and sensitivity are interrelated.
Don’t use analytical balance to weigh samples in the kilogram range and vice versa.
Choose best balance – not simplest to operate.

## Slide 18: III PROPER OPERATION; AVOIDING ERRORS
Accuracy and precision of modern balances is primarily affected by:
  User technique and lab conditions
  Maintenance
  Design and construction of balance
Accuracy and precision of instruments is excellent

## Slide 19: OPERATING AN ELECTRONIC ANALYTICAL BALANCE
    1. Level balance.
    2. Adjust the balance to zero with pan clean and empty and chamber doors closed.
    3. Tare the weighing container or weigh the empty vessel.
    4. Place sample on weighing pan; read the value for the measurement.
    5. Remove sample, clean.

## Slide 20: WAYS TO GET SYSTEMATIC ERROR:
Don’t level the balance
Don’t adjust to zero
Allow vibration
Don’t close balance doors
Touch samples and their containers
Allow temperature to fluctuate

## Slide 21
Ignore static charge
Ignore loss or gain of moisture
Place overload on weighing pan
Select wrong weighing vessel
Make a mess and don’t clean up

## Slide 22: MAINTENANCE AND CALIBRATION
Calibration brings balance readings into accordance with internationally accepted standards.
Calibration must be periodically checked in the laboratory of the user.

## Slide 23: CALIBRATION
Level balance
Set to zero
Place standard on balance, often 100 g
Adjust to upper weight

## Slide 24: STANDARDS
Calibrate with standards; metal objects whose masses are known (within limits of uncertainty).
Accuracy of any weight determination is limited by the accuracy of the standards used for comparison.

## Slide 25
Standard weights need to be periodically recertified since change over time

## Slide 26: QUALITY PROGRAM
Calibrate periodically.
Check precision and linearity periodically.
Consistently check and record weights of standards – tests accuracy.
Follow SOPS ( standard operating procedures)

## Slide 27: LINEARITY
Linearity error occurs when a balance is properly calibrated at zero and full-scale (the top of its range) but the values obtained for weights in the middle of the scale are not exactly correct.
If a balance has linearity error, have it repaired professionally.
Practice in lab today.

## Slide 28: IV MASS versus WEIGHT
Value read from a balance is the weight of an object, not its mass.
May seem surprising. After all, the object is directly compared to a standard whose mass is known.

## Slide 29: When weighing we should consider the followings:
Draughts
Level surface
Vibration
Temperature
Humidity
Electrical interference
magnetic fields

## Slide 30: Analytical balance(sensitive balance)